Q2
  For input power 45mW;

    efficiency = P_radiated/P_input

        0.9 = P_radiated/45

   P_radiated = (0.9*45)

   Directivity = 4π (Max. radiation intensity)/Total radiated power

        = 4π*100/(0.9*45)

        = 9.87π

    Antenna Gain = Antenna efficiency * Antenna Directivity

        = 0.9*9.87π

        = 8.88π

When radiated power is 45mW

 Directivity = 4π (Max. radiation intensity)/Total radiated power

        = 4π * 100/45

        = 8.89π

Antenna Gain = Antenna efficiency * Antenna Directivity

        = 0.9 * 8.89π

        = 8π