Stage 1 at the attenuator

  Let output power Po from the expression

     -3dB = 10log ((150*10^-3)/Po)

        Po = 0.3W

Stage 2 Amplification
let output be P1

 from,
        -20dB = 10log(P1/0.3)

        P1 = 0.003W

Stage 3 Amplification
let output power be Pout

From,

 5dB = 10log(Pout/0.003)

Pout = 9.489mW